# Process
## Overall
The overall process has a few steps:

Obfuscation:
1. Data Setup, which includes the following steps:
  1. Read data into a matrix
  2. (Optionally) pad data with bogus data to increase entropy, bogus data can be of similar structure to the original data.
2. Data Scramble
3. Output obfuscated file and key file
Decoding:
1. Data read back into the matrix, height and width of overall matrix is read from key file.
2. Scrambling steps are performed in reverse, effectively unscrambling the data
3. Unscrambled data is taken from the subset of the overall matrix (to avoid gleaning any of the dummy data). The length and width of the original data matrix size is gotten from the key file

The process starts by the program accepting a set of data. This data is placed into a rectangular matrix, with each node in the matrix holding a single bit of the information given. The length and width of this data is noted for later. This data in the matrix is then padded with bogus data on the bottom and left side of the matrix, adding entropy into the system.
Then, the data is scrambled using a series of steps. There are a few different moves that can be taken, outlined more below. As moves are made, they are recorded for the key file. Once the data has been scrambled to the satisfaction of the program (implementation dependent), the program writes it out to a “.obfd” file (obfuscated data), along with a key file “.obfdk” (obfuscated data key). At this point, the data should be saved in a way that should not be able to be read or otherwise gleaned.

# Data Structure

# Scrambling

# Scrambled Data File

# Key File

## Overall
The key file is the file generated by the process that contains the steps used to scramble the data, and meta-data about the scrambled data. The steps are performed in reverse on the data to unscramble it.

The key file also contains information about the dimensions of the data, such as length and width of the matrix used.

It should be noted that while whitespace is allowed, it is disregarded when parsed.

## Structure

The key file is structured as having two sections:
1. Meta
2. Scramble

Sections are denoted by labels in the file, and enclosed by curly brackets. Example:

<section name>{<entries for section>}

An example of a key file might be:

(begin example file)
meta{
<metadata for file>
}
scramble {
<steps used for scramble>
}
(end example file)

## Meta Section

The meta section is what describes general details surrounding the scramble. An example of metadata include the original size of the data. This metadata is described in the standard json format for easy processing. There are both required and not required metadata. Required metadata is required because it is what tells the implementation how to process and descramble the data. Different implementations can add their own metadata to this section, but these extra entries should not interfere with the scramble (a different implementation that does not use these extra entries should still be able to descramble with the same key file)

Example meta section:

meta{
“origWidth”:50,
“origHeight”:50,
}

### Valid “Canonical” Metadata
These are the metadata values that all implementations are to support.
Req	Key	Value Type	Optional Values (if applicable)	Description
Y	origHeight	Long (64 bit integer)	N/A	The height of the original data in the initial dataset
Y	origWidth	Long (64 bit integer)	N/A	The with of the original data in the initial dataset
Y	nodeType	String	Byte, Bit	The type of node used to scramble. Either a node will hold a bit, etc

## Scramble Section

The moves taken by the scrambler are recorded as the key.
The recorded moves are case insensitive.
Moves are listed in prefix notation, separated by semicolons (;).
Whitespace is optional; ignored in parsing.

The list is comprised of the moves used backwards; the list starts with the last move applied to the matrix and ends with the first one. Moves in the list describe the steps needed to return to the original state.

General syntax as follows:

<operation>:<a number of operands, comma separated>;

### Move List
These are the valid moves that an implementation is allowed to make.
# (OpCode)	Move	Syntax	Description	Regex
1	Swap individual blocks	Sw:<x1#>x<y1#>, <x2#>x<y2#>;	Swaps two blocks in the matrix.	\s*(1|sw)\s*:\s*\d+\s*x\s*\d+\s*,\s*\d+\s*x\s*\d+\s*;\s*
2	Swap Rows	SwR:<y1#>,<y2#>;	Swaps two rows in the matrix	\s*(2|swr)\s*:\s*\d+\s*,\s*\d+\s*;\s*
3	Swap Columns	SwC:<x#>,<x2#>;	Swaps two columns in the matrix	\s*(3|swc)\s*:\s*\d+\s*,\s*\d+\s*;\s*
4	Slide Row	SlR:<y#>,<# of units to slide down>;	Slides a row a certain number units. The blocks that slide off the end of the matrix get put at the beginning.	\s*(4|slr)\s*:\s*\d+\s*,\s*-?\d+\s*;\s*
5	Slide Column	SlC:<x#>,<# of units to slide>;	Slides a column a certain number units. The blocks that slide off the end of the matrix get put at the beginning.	\s*(5|slc)\s*:\s*\d+\s*,\s*-?\d+\s*;\s*
6	Rotate Box Clockwise	Rcl: <# 90 deg rot>,<right top corner x>x<right top corner y>, <left bot corner x>x<left bot corner y>;	Rotates a box of blocks some multiple of 90 degrees clockwise. Accepts rectangles. Box denoted by top right and bottom left corners.	\s*(6|rcl)\s*:\s*(-?1|-?2|-?3)\s*,\s*\d+\s*x\s*\d+\s*,\s*\d+\s*x\s*\d+\s*;\s*
7	Rotate Box Counter Clockwise	Rcc: <# 90 deg rot>,<right top corner x>x<right top corner y>, <left bot corner x>x<left bot corner y>;	Rotates a box of blocks some multiple of 90 degrees counter clockwise. Accepts rectangles. Box denoted by top right and bottom left corners.	\s*(7|rcc)\s*:\s*(-?1|-?2|-?3)\s*,\s*\d+\s*x\s*\d+\s*,\s*\d+\s*x\s*\d+\s*;\s*